## Slide 1
1.1.1 Structure and Function of the Processor
OCR H446 — Component 01
Week 02 (07 Sep)

## Slide 2
Learning objectives
By the end of this lesson you can:
  I can describe the roles of the ALU, Control Unit and the registers PC, MAR, MDR, CIR and ACC
  I can trace the fetch-decode-execute cycle, naming every register transfer and bus involved
  I can explain how clock speed, cores, cache and pipelining affect CPU performance, with caveats
  I can compare Von Neumann, Harvard and contemporary (modified Harvard) architectures with distinct differences

## Slide 3
Do Now — retrieval starter
1. Convert the denary number 13 into 8-bit binary.
2. Convert the binary number 10110 into denary.
3. From GCSE: what is the overall job of the CPU in a computer system?
4. From GCSE: state one difference between RAM and ROM.
5. From GCSE: what is an algorithm?

## Slide 4
Do Now — answers
1. Convert the denary number 13 into 8-bit binary.
  Answer: 00001101 (8 + 4 + 1 = 13).
2. Convert the binary number 10110 into denary.
  Answer: 22 (16 + 4 + 2).
3. From GCSE: what is the overall job of the CPU in a computer system?
  Answer: It fetches, decodes and executes instructions, processing data and controlling the rest of the system.
4. From GCSE: state one difference between RAM and ROM.
  Answer: RAM is volatile working memory that can be read and written; ROM is non-volatile and holds fixed startup instructions.
5. From GCSE: what is an algorithm?
  Answer: A precise sequence of steps that solves a problem or completes a task.

## Slide 5
Key terminology
ALU — Arithmetic Logic Unit; performs arithmetic, logic and shift operations, sending results to the accumulator.
Control Unit (CU) — Decodes instructions, generates control signals and synchronises the CPU using the clock.
Program Counter (PC) — Register holding the address of the next instruction to fetch; incremented every cycle.
MAR — Memory Address Register; holds the address of the memory location to be read from or written to.
MDR — Memory Data Register; holds the data or instruction just fetched from, or about to be written to, memory.
CIR — Current Instruction Register; holds the instruction currently being decoded and executed.
Cache — Small, very fast memory on or near the CPU holding frequently used data and instructions; not part of RAM.
Pipelining — Overlapping the fetch, decode and execute stages of consecutive instructions to raise throughput.
Von Neumann architecture — A single shared memory and bus for both data and instructions.

## Slide 6
The big picture: what the processor does
The CPU repeatedly fetches an instruction from memory, decodes it, then executes it
This loop is the fetch-decode-execute (FDE) cycle, running billions of times per second
Both instructions and data live in main memory as binary; the CPU cannot tell them apart by looking
Inside the CPU: the ALU, the Control Unit, and a set of registers
Everything this lesson builds on this one loop: fetch, decode, execute, repeat.

## Slide 7
The ALU and the Control Unit
The ALU performs arithmetic (add, subtract, multiply, divide), logic (AND, OR, NOT, comparisons) and shifts
ALU results are placed in the accumulator (ACC)
The Control Unit decodes each instruction and generates control signals directing the other components
The CU manages the flow of data on the buses and synchronises everything with the clock

## Slide 8
The five special-purpose registers
A register is a tiny, extremely fast storage location inside the CPU
PC: address of the NEXT instruction; incremented each cycle
MAR: the address being read from or written to; MDR: the data or instruction itself
CIR: the current instruction while it is decoded and executed
ACC: the immediate result of ALU calculations
MAR holds an ADDRESS, MDR holds DATA. Swapping these is the most common lost mark.

## Slide 9
The three system buses
Address bus: carries addresses from CPU to memory; UNIDIRECTIONAL
Data bus: carries data and instructions between CPU and memory; bidirectional
Control bus: carries control signals such as read, write and clock; bidirectional
An address bus n bits wide can address 2^n memory locations

## Slide 10
FDE cycle: the fetch stage in full
The contents of the PC are copied into the MAR
A read signal is sent on the control bus; the instruction returns along the data bus into the MDR
The PC is incremented so it points at the following instruction
The instruction is copied from the MDR into the CIR
  MAR = PC
  MDR = contents of memory at address in MAR
  PC = PC + 1
  CIR = MDR
Candidates routinely miss the PC increment and the MDR to CIR copy — include both.

## Slide 11
FDE cycle: decode and execute
Decode: the CU splits the CIR contents into opcode (the operation) and operand (data or an address)
Execute an ALU operation: values are processed and the result goes to the ACC
Execute a load or store: data moves between memory and registers via MAR and MDR
Execute a jump or branch: a new address is written into the PC, changing what fetches next

## Slide 12
Performance factor 1: clock speed and cores
The clock sends regular pulses; speed in Hz is pulses per second
Higher clock speed means more FDE cycles per second, but heat and power consumption set a limit
A core is an independent processing unit running its own FDE cycle
More cores only help if the task can be split up AND the software supports multiple cores

## Slide 13
Performance factor 2: cache
Cache is small, very fast memory on or near the CPU holding frequently or recently used data
It is separate fast memory, NOT a section of RAM
Checked in order: L1 (smallest, fastest) then L2 then L3 (largest, slowest) then RAM
More cache means fewer slow trips to RAM, so the CPU waits less

## Slide 14
Performance factor 3: pipelining
Pipelining overlaps the fetch, decode and execute stages of consecutive instructions
While instruction 1 executes, instruction 2 decodes and instruction 3 is fetched
Throughput rises, but no individual instruction completes any faster
Jumps and branches cause hazards: prefetched instructions become wrong and must be flushed

## Slide 15
Von Neumann, Harvard and contemporary CPUs
Von Neumann: ONE shared memory and bus for data and instructions; simpler, cheaper, flexible; general-purpose PCs
Its weakness is the bottleneck: it cannot fetch an instruction and access data simultaneously
Harvard: SEPARATE memories and buses, allowing simultaneous instruction fetch and data access; costlier; embedded systems, microcontrollers, DSPs
Contemporary CPUs are modified (hybrid) Harvard: unified main memory but separate L1 instruction and data caches
This hybrid point IS spec bullet 1.1.1(e) — contemporary processor architecture.

## Slide 16
Worked example 1
Full register-transfer trace of fetching one instruction
  1. Suppose PC holds address 0052 and location 0052 contains the instruction ADD 13
  2. Step 1: PC copied to MAR, so MAR now holds 0052
  3. Step 2: read signal sent on the control bus; ADD 13 travels along the data bus into the MDR
  4. Step 3: PC incremented, so PC now holds 0053
  5. Step 4: MDR copied to CIR, so CIR now holds ADD 13
  6. Decode: the CU splits ADD 13 into opcode ADD and operand 13
  7. Execute: the value at address 13 is fetched (via MAR and MDR again), the ALU adds it to the ACC, and the result stays in the ACC

## Slide 17
Worked example 2
Address bus width calculation
  1. Question: a CPU has a 16-bit address bus. How many memory locations can it directly address?
  2. Rule: an n-bit address bus addresses 2^n locations
  3. Calculation: 2^16 = 65,536 locations
  4. Extension: widening the bus to 17 bits DOUBLES this to 131,072, because each extra bit doubles the address space
  5. Common error: answering 16 x 2 or 2 x 16 instead of 2 to the power 16

## Slide 18
Worked example 3
Pipelining throughput: 6 instructions, 3 stages
  1. Without pipelining, each instruction needs 3 cycles (fetch, decode, execute) before the next starts: 6 x 3 = 18 cycles
  2. With pipelining, a new instruction enters the pipeline every cycle once it is full
  3. Cycle 1: I1 fetches. Cycle 2: I1 decodes, I2 fetches. Cycle 3: I1 executes, I2 decodes, I3 fetches
  4. First instruction finishes at cycle 3; one more finishes every cycle after: cycles 3,4,5,6,7,8
  5. Total = 8 cycles (formula: instructions + stages - 1 = 6 + 3 - 1)
  6. Note: each instruction still takes 3 cycles of its own — latency is unchanged, throughput improves

## Slide 19
Activity 1
Living FDE Cycle (unplugged role-play) (15 min)
  Assign roles with labels: PC, MAR, MDR, CIR, CU, ALU, ACC, plus students at numbered desks as Memory holding instruction cards (LDA 12, ADD 13, STA 14, HLT)
  Walk the fetch: PC shows their number to MAR; MAR calls the address down the one-way address bus; Memory hands the card to MDR via the data bus; PC increments; MDR passes the card to CIR
  CU takes the card from CIR, splits it aloud into opcode and operand, and directs the execute: loads go via MDR to ACC; ADD sends both values to the ALU, who hands the result to ACC
  Ban illegal moves: if data travels a route that does not exist (Memory talking straight to CIR, or Memory speaking back up the address bus), freeze and make the class spot it
  Round 2: swap roles and include a branch instruction — the class must realise execute writes a new address into the PC
Stretch: Ask the branching PC-holder: what happens to the two instructions a pipeline would already have prefetched? (Flushed — branch hazard.)

## Slide 20
Activity 2
Human Pipeline Laundry Line (10 min)
  Set up three desks labelled FETCH, DECODE, EXECUTE; teacher claps to mark each clock cycle
  Round 1, no pipelining: one instruction card at a time passes through all three desks before the next starts; class counts claps for 6 cards (18)
  Round 2, pipelining: three volunteers, one per desk; every clap each desk passes its card forward and FETCH takes a new one; count again (8)
  Ask: did any single instruction get faster? No — latency unchanged, throughput improved
  Round 3: make card 3 a branch; when it executes, the cards in FETCH and DECODE are thrown away (pipeline flush) and the class recounts
Stretch: Instruction 4 needs the result of instruction 3, which has not executed yet — what are the CPU's options? (Stall, or predict/reorder.)

## Slide 21
Activity 3
Always-Sometimes-Never: CPU Performance (10 min)
  Display one statement at a time; pairs discuss for 30 seconds then show A, S or N on whiteboards simultaneously
  Statements: doubling clock speed doubles program speed; a quad-core beats a dual-core; the address bus carries data to memory; a cache miss means fetching from RAM; increasing address bus width increases addressable memory; pipelining makes each instruction faster
  Pick a pair from each camp to justify; every Sometimes must state when it is true and when false
  Answers: Sometimes (bottlenecks, heat); Sometimes (only if parallelisable and software supports it); Never (addresses only, one-way); Sometimes (L2 or L3 may hit first); Always (2^n); Never (throughput rises, latency does not)
  Close: pairs convert one Sometimes into an Always by adding the missing caveat
Stretch: Write one Sometimes statement about cache levels that would split the class.

## Slide 22
Practice (1-4)
1. Describe the steps of the fetch phase of the fetch-decode-execute cycle, naming the registers and buses used. [4]
2. State the purpose of the MAR and the MDR. [2]
3. Describe the role of the program counter, including what happens to it during a jump instruction. [3]
4. A CPU has a 24-bit address bus. Calculate the number of memory locations it can directly address. [2]

## Slide 23
Practice — answers (1-4)
1. Describe the steps of the fetch phase of the fetch-decode-execute cycle, naming the registers and buses used. [4]
  Answer: The contents of the PC are copied into the MAR (1); a read signal is sent along the control bus and the instruction is transferred from memory along the data bus into the MDR (1); the PC is incremented to point to the next instruction (1); the instruction is copied from the MDR into the CIR (1).
2. State the purpose of the MAR and the MDR. [2]
  Answer: The MAR holds the address of the memory location to be read from or written to (1); the MDR holds the data or instruction that has been fetched from, or is about to be written to, that location (1).
3. Describe the role of the program counter, including what happens to it during a jump instruction. [3]
  Answer: The PC holds the address of the next instruction to be fetched (1); it is incremented during each fetch so it points to the following instruction (1); executing a jump writes a new address into the PC so execution continues from a different location (1).
4. A CPU has a 24-bit address bus. Calculate the number of memory locations it can directly address. [2]
  Answer: 2^24 (1) = 16,777,216 locations (1).

## Slide 24
Practice (5-8)
1. Explain why increasing the number of cores does not always make a program run faster. [3]
2. Explain how cache improves the performance of the CPU. [3]
3. Describe how pipelining increases the throughput of a processor and explain why a branch instruction reduces this benefit. [4]
4. Compare Von Neumann and Harvard architectures, and state how contemporary processors combine the two. [6]

## Slide 25
Practice — answers (5-8)
1. Explain why increasing the number of cores does not always make a program run faster. [3]
  Answer: The program or task may not be parallelisable, e.g. each step depends on the previous result (1); the software must be written to use multiple cores/threads, otherwise extra cores sit idle (1); coordinating and combining results between cores adds overhead, limiting the gain (1).
2. Explain how cache improves the performance of the CPU. [3]
  Answer: Cache is small, very fast memory on or near the CPU (1); it stores frequently or recently used data and instructions (1); these can be accessed far faster than fetching from RAM, so the CPU spends less time waiting (1).
3. Describe how pipelining increases the throughput of a processor and explain why a branch instruction reduces this benefit. [4]
  Answer: Pipelining overlaps the fetch, decode and execute stages of consecutive instructions (1), so one instruction can complete per clock cycle once the pipeline is full, raising throughput (1). A branch changes the PC to a new address (1), so the instructions already prefetched into the pipeline are wrong and must be flushed, wasting cycles (1).
4. Compare Von Neumann and Harvard architectures, and state how contemporary processors combine the two. [6]
  Answer: Von Neumann has a single shared memory and bus for data and instructions (1) so it cannot fetch an instruction and access data simultaneously, causing a bottleneck (1), but is simpler/cheaper and used in general-purpose PCs (1). Harvard has separate memories and buses for data and instructions (1) allowing simultaneous access, and is used in embedded systems and DSPs (1). Contemporary CPUs are modified Harvard: unified main memory but separate L1 instruction and data caches (1).

## Slide 26
Common misconceptions
✗ Students often think the MAR holds data and the MDR holds addresses; it is the reverse — MAR is the ADDRESS register, MDR is the DATA register.
✗ Students often think cache is a reserved section of RAM, but it is separate, much faster memory located on or near the CPU itself.
✗ Students often think more cores always means proportionally faster, but the gain depends on the task being parallelisable and the software supporting it.
✗ Students often think pipelining makes each instruction execute faster, but latency per instruction is unchanged; only throughput improves.
✗ Students often think all three buses are two-way, but the address bus is unidirectional, carrying addresses from the CPU to memory only.

## Slide 27
How the exam asks this
Command words: State (1 mark definitions of registers), Describe (fetch stage, 3-4 marks), Explain (performance factors, 2-3 marks each), Compare/Discuss (architectures or buying advice, up to 9-mark levels of response).
The FDE trace is a classic 4-6 marker: marks are lost by omitting the PC increment and the MDR to CIR copy.
9-mark example stem: 'A gamer is choosing between a 3.2 GHz quad-core CPU with 8 MB cache and a 4.0 GHz dual-core with 2 MB cache. Discuss which is more suitable.' — answers must weigh clock, cores, cache AND the software caveat.
Calculation questions use 2^n for addressable locations; always show the power, not just the final value.

## Slide 28
Your turn
Task
  Write a full register-transfer trace for the two-instruction program LDA 20 then ADD 21, where address 20 holds 7 and address 21 holds 5. For each instruction give every fetch step (naming registers and buses), the decode split, and the execute action, finishing with the value left in the ACC (12).
Challenge / stretch
  A CPU has a 20-bit address bus and a 3-stage pipeline. Calculate the addressable locations (2^20 = 1,048,576), then calculate how many cycles 10 instructions take unpipelined (30) versus pipelined (12), and explain why a branch at instruction 5 would add wasted cycles.

## Slide 29
Exit ticket
1. Name the two fetch-stage steps that candidates most often forget.
2. Which bus is unidirectional and what does it carry?
3. How do contemporary CPUs mix Von Neumann and Harvard designs?

## Slide 30
Exit ticket — answers
1. Name the two fetch-stage steps that candidates most often forget.
  Answer: Incrementing the PC, and copying the instruction from the MDR into the CIR.
2. Which bus is unidirectional and what does it carry?
  Answer: The address bus; it carries memory addresses from the CPU to memory only.
3. How do contemporary CPUs mix Von Neumann and Harvard designs?
  Answer: They use one unified main memory (Von Neumann) but separate L1 instruction and data caches (Harvard) — modified Harvard.