## Slide 1
1.4.3 Boolean Algebra (part 1)
OCR H446 — Component 01
Week 21 (22 Feb)

## Slide 2
Learning objectives
By the end of this lesson you can:
  I can state the truth tables for AND, OR, NOT and XOR and recognise their circuit symbols.
  I can combine gates into circuits and construct truth tables for 2- and 3-input expressions using working columns.
  I can state and apply the Boolean identities: commutation, association, distribution, absorption and double negation.
  I can apply De Morgan's laws and simplify Boolean expressions, naming the law used at each step.

## Slide 3
Do Now — retrieval starter
1. From 1.4.2: which traversal of a binary search tree outputs the values in ascending order?
2. From 1.4.2: a hash table uses index = key MOD 7. Keys 15 and 22 are inserted. What happens?
3. From 1.4.2: in a BST, where would 65 be inserted given root 50 with right child 70 and 70's left child 60?
4. From 1.4.1: convert denary 45 to 8-bit unsigned binary.
5. From 1.4.1: give the 8-bit two's complement representation of -6.

## Slide 4
Do Now — answers
1. From 1.4.2: which traversal of a binary search tree outputs the values in ascending order?
  Answer: In-order traversal (left subtree, root, right subtree).
2. From 1.4.2: a hash table uses index = key MOD 7. Keys 15 and 22 are inserted. What happens?
  Answer: Both hash to 1 (15 MOD 7 = 1, 22 MOD 7 = 1): a collision, resolved by e.g. linear probing or chaining.
3. From 1.4.2: in a BST, where would 65 be inserted given root 50 with right child 70 and 70's left child 60?
  Answer: Walk 50 (go right), 70 (go left), 60 (go right): 65 becomes the right child of 60.
4. From 1.4.1: convert denary 45 to 8-bit unsigned binary.
  Answer: 00101101 (32 + 8 + 4 + 1 = 45).
5. From 1.4.1: give the 8-bit two's complement representation of -6.
  Answer: +6 is 00000110; invert to 11111001, add 1: 11111010 (check: -128 + 64 + 32 + 16 + 8 + 2 = -6).

## Slide 5
Key terminology
Logic gate — An electronic component that takes one or more binary inputs and produces one binary output.
Truth table — A table listing the output of a gate or expression for every possible combination of inputs.
XOR (exclusive OR) — Gate written A ⊻ B that outputs 1 only when its two inputs differ.
Boolean expression — A combination of Boolean variables and operators (∧, ∨, ¬, ⊻) that evaluates to 0 or 1.
Commutative law — Order of inputs does not matter: A ∧ B = B ∧ A and A ∨ B = B ∨ A.
Associative law — Grouping does not matter for one operator: (A ∧ B) ∧ C = A ∧ (B ∧ C), likewise for ∨.
Distributive law — A ∧ (B ∨ C) = (A ∧ B) ∨ (A ∧ C), and A ∨ (B ∧ C) = (A ∨ B) ∧ (A ∨ C).
Absorption law — A ∨ (A ∧ B) = A and A ∧ (A ∨ B) = A; the redundant term is absorbed.
De Morgan's laws — ¬(A ∧ B) = ¬A ∨ ¬B and ¬(A ∨ B) = ¬A ∧ ¬B: break the bar, swap the operator, negate each term.

## Slide 6
Boolean algebra and OCR notation
Boolean values are 1 (true) and 0 (false); expressions built from them describe circuit outputs.
OCR exam notation: ∧ means AND, ∨ means OR, ¬ means NOT, ⊻ means XOR.
So ¬A ∧ (B ∨ C) reads: NOT A, AND, open bracket B OR C close bracket.
Every expression can be drawn as a circuit of gates and summarised in a truth table.
Electronics texts write A·B for A ∧ B and A+B for A ∨ B — identical operations, different symbols.

## Slide 7
The NOT and AND gates
NOT takes a single input and inverts it: ¬0 = 1 and ¬1 = 0.
NOT symbol: a triangle pointing right with a small negation circle on its output.
A ∧ B outputs 1 only when both inputs are 1: rows 00, 01, 10 give 0; only 11 gives 1.
AND symbol: a D-shape, flat edge on the input side, curved edge to the output.
Think of AND as multiplication: 1 × 1 = 1, anything with a 0 gives 0.

## Slide 8
The OR and XOR gates
A ∨ B outputs 1 when at least one input is 1: rows 01, 10, 11 give 1; only 00 gives 0.
OR symbol: a curved shield shape with a concave input edge and pointed output.
A ⊻ B (exclusive OR) outputs 1 only when the inputs differ: rows 01 and 10 give 1.
XOR symbol: the OR shape with an extra curved line across the inputs.
OR and XOR differ in exactly one row: when both inputs are 1, OR gives 1 but XOR gives 0.

## Slide 9
Combining gates into circuits
An expression is a wiring diagram in disguise: each operator is a gate.
(A ∧ B) ∨ ¬C needs three gates: an AND fed by A and B, a NOT fed by C, an OR fed by both outputs.
Brackets show which gate output feeds which gate input; evaluate innermost brackets first.
¬ applies before ∧ and ∨, so ¬A ∧ B means (¬A) ∧ B, not ¬(A ∧ B).
Exam questions run both ways: expression to circuit diagram, and circuit diagram to expression.

## Slide 10
Truth tables for two-input expressions
Two inputs give 2 to the power 2 = 4 rows; list them in binary counting order 00, 01, 10, 11.
Add a working column for each sub-expression before the final output column.
Example ¬A ∧ B: working column ¬A reads 1, 1, 0, 0 down the rows.
Final column: only row A = 0, B = 1 outputs 1; the other three rows output 0.

## Slide 11
Truth tables for three-input expressions
Three inputs give 2 to the power 3 = 8 rows; count in binary from 000 to 111.
Fill the columns pattern-wise: A runs 0000 1111, B runs 0011 0011, C runs 0101 0101.
One working column per gate; the final column is the circuit output Q.
Spot-check one row by hand: for Q = (A ∧ B) ∨ ¬C at row 110, A ∧ B = 1, ¬C = 1, so Q = 1.
Missing rows or wrong row order is the most common way to drop truth-table marks.

## Slide 12
Identities: commutation, association, distribution
Commutation: A ∧ B = B ∧ A and A ∨ B = B ∨ A; input order never matters.
Association: (A ∧ B) ∧ C = A ∧ (B ∧ C), and the same for ∨; regrouping is free.
Distribution: A ∧ (B ∨ C) = (A ∧ B) ∨ (A ∧ C), like expanding brackets in maths.
Unlike ordinary algebra, OR also distributes over AND: A ∨ (B ∧ C) = (A ∨ B) ∧ (A ∨ C).

## Slide 13
Identities: absorption, double negation and the basics
Absorption: A ∨ (A ∧ B) = A and A ∧ (A ∨ B) = A; the longer term is swallowed.
Double negation: ¬¬A = A; always use it to tidy after De Morgan's.
Identity and null: A ∧ 1 = A, A ∨ 0 = A, A ∧ 0 = 0, A ∨ 1 = 1.
Complement: A ∨ ¬A = 1 and A ∧ ¬A = 0; idempotence: A ∧ A = A, A ∨ A = A.

## Slide 14
De Morgan's laws
¬(A ∧ B) = ¬A ∨ ¬B, and ¬(A ∨ B) = ¬A ∧ ¬B.
Method: break the bar, swap the operator (∧ to ∨ or ∨ to ∧), negate each term.
You must do both: swapping the operator without negating each variable is the classic error.
Check any claimed law with one truth-table row: at A = 1, B = 0, ¬(A ∧ B) = 1 but ¬A ∧ ¬B = 0.
¬(A ∧ B) = ¬A ∧ ¬B is wrong: the operator must change when the bar breaks.

## Slide 15
Simplifying expressions: the method
Name the law at every step; the working earns marks, not just the answer.
Order of attack: De Morgan's to push negations inward, double negation to tidy, then distribute and absorb.
Look for complements appearing: B ∨ ¬B = 1 and B ∧ ¬B = 0 collapse whole terms.
Verify the result by testing one or two truth-table rows against the original.
Fewer operators means fewer gates: simplification cuts circuit cost, an exam-favourite justification.

## Slide 16
Worked example 1
Truth table for Q = (A ∧ B) ∨ ¬C, all eight rows
  1. Three inputs, so 8 rows counting 000 to 111; working columns for A ∧ B and ¬C.
  2. A ∧ B column: 0, 0, 0, 0, 0, 0, 1, 1 (only rows 110 and 111 have A = B = 1).
  3. ¬C column: 1, 0, 1, 0, 1, 0, 1, 0 (inverts the alternating C column).
  4. Q is the OR of the two working columns, row by row.
  5. Rows 000, 010, 100: A ∧ B = 0 but ¬C = 1, so Q = 1; rows 110 and 111: A ∧ B = 1, so Q = 1.
  6. Rows 001, 011, 101: A ∧ B = 0 and ¬C = 0, so Q = 0.
  7. Final Q column down the rows: 1, 0, 1, 0, 1, 0, 1, 1. Q is 0 exactly when C = 1 and A ∧ B = 0.

## Slide 17
Worked example 2
Simplifying ¬(¬A ∨ B) with De Morgan's law
  1. Start with ¬(¬A ∨ B): an outer negation over an OR.
  2. De Morgan's law: break the bar, change ∨ to ∧, negate each term: ¬(¬A) ∧ ¬B.
  3. Double negation: ¬(¬A) = A, giving A ∧ ¬B.
  4. Check with a truth table: ¬A ∨ B is 0 only at A = 1, B = 0, so its negation is 1 only there.
  5. A ∧ ¬B is also 1 only at A = 1, B = 0: the two expressions match on all four rows.
  6. Final answer: A ∧ ¬B, using De Morgan's law then double negation.

## Slide 18
Worked example 3
Simplifying (A ∧ B) ∨ (A ∧ ¬B) ∨ (¬A ∧ B), naming every law
  1. Factor A from the first two terms using distribution: A ∧ (B ∨ ¬B), leaving ∨ (¬A ∧ B).
  2. Complement law: B ∨ ¬B = 1, so the first part becomes A ∧ 1.
  3. Identity law: A ∧ 1 = A. The expression is now A ∨ (¬A ∧ B).
  4. Distribution of ∨ over ∧: A ∨ (¬A ∧ B) = (A ∨ ¬A) ∧ (A ∨ B).
  5. Complement law: A ∨ ¬A = 1, then identity law: 1 ∧ (A ∨ B) = A ∨ B.
  6. Verify against the original: row 00 gives 0 ∨ 0 ∨ 0 = 0; rows 01, 10, 11 give 1 (terms ¬A ∧ B, A ∧ ¬B, A ∧ B fire respectively).
  7. That is exactly A ∨ B: 0 only at row 00. Final answer: A ∨ B.

## Slide 19
Activity 1
The Circuit Walk (human logic gates) (15 min)
  Build Q = (A ∧ B) ∨ ¬C with students: inputs A, B, C at one wall; an AND student fed by A and B; a NOT student fed by C; an OR student fed by both gate outputs.
  Each gate student states their rule aloud, e.g. I output 1 only if BOTH my inputs are 1.
  Inputs hold up 0/1 cards and signals propagate by walking cards to each gate; the class predicts Q on mini-whiteboards before the signal reaches OR.
  Run rows (1,0,0), (1,1,1), (0,1,1), (0,0,0): Q = 1, 1, 0, 1. Swap students between roles each row.
  Round 2: build ¬(A ∧ B) and ¬A ∨ ¬B side by side with two teams and race all four input rows; both circuits give 1, 1, 1, 0, a living proof of De Morgan's law.
Stretch: Ask each team to predict, before running it, one input row where the two circuits would differ if De Morgan's swapped the operator but forgot to negate each input; then test it.

## Slide 20
Activity 2
Always-Sometimes-Never: Boolean claims (12 min)
  Pairs classify each claim as Always, Sometimes or Never true, proving it: a named law for Always/Never, concrete A/B values (one working, one failing) for Sometimes.
  Claims: (a) A ∨ ¬A = 1; (b) A ∧ B = A; (c) ¬(A ∧ B) = ¬A ∧ ¬B; (d) A ∨ (A ∧ B) = A; (e) A ⊻ A = 1; (f) A ∨ 1 = 1.
  Reveal one at a time; a pair presents their proof while the class hunts for counterexamples.
  Answers: (a) Always, complement law; (b) Sometimes, true at A=0 or B=1, false at A=1 B=0; (c) Sometimes, the classic De Morgan's error, true at A=B=0, false at A=0 B=1; (d) Always, absorption; (e) Never, XOR of identical inputs is always 0; (f) Always, null law.
Stretch: Pairs repair every Sometimes or Never claim into a genuine identity, e.g. (c) becomes ¬(A ∧ B) = ¬A ∨ ¬B and (e) becomes A ⊻ A = 0.

## Slide 21
Activity 3
Simplification Surgery (grade the mock answers) (12 min)
  Announce: five simplifications from last year's mock, some right, some wrong; pairs grade each and rewrite any wrong right-hand side.
  The five: (1) ¬(A ∨ B) = ¬A ∨ ¬B; (2) A ∨ (¬A ∧ B) = A ∨ B; (3) A ∧ (A ∨ B) = A ∧ B; (4) ¬(¬A ∧ B) = A ∨ ¬B; (5) A ⊻ B = (A ∧ B) ∨ (¬A ∧ ¬B).
  Whiteboards up; tally verdicts, then settle contested lines with a single truth-table row or a named law.
  Answers: (1) wrong, De Morgan's gives ¬A ∧ ¬B; (2) correct; (3) wrong, absorption gives A (test A=1, B=0); (4) correct by De Morgan's plus double negation; (5) wrong, that is XNOR; XOR = (A ∧ ¬B) ∨ (¬A ∧ B), test A=B=1.
  Debrief the two big traps: De Morgan's changes the operator AND negates each variable; and plausible answers deserve a truth-table spot check.
Stretch: Pairs simplify ¬(¬A ∨ ¬B) ∨ (A ∧ ¬B) fully and prove it equals A, naming De Morgan's, distribution, complement and identity.

## Slide 22
Practice (1-4)
1. Complete the truth table for A ⊻ B. [2]
2. Simplify ¬(¬A) ∨ (B ∧ ¬B), naming the law used at each step. [3]
3. Use De Morgan's law to rewrite ¬(A ∨ ¬B) without a bracket. [2]
4. State the input combinations for which Q = ¬A ∧ (B ∨ C) is 1. [2]

## Slide 23
Practice — answers (1-4)
1. Complete the truth table for A ⊻ B. [2]
  Answer: Rows in order 00, 01, 10, 11 give outputs 0, 1, 1, 0 (1 mark for rows 01 and 10 correct, 1 mark for rows 00 and 11 correct). XOR is 1 only when the inputs differ.
2. Simplify ¬(¬A) ∨ (B ∧ ¬B), naming the law used at each step. [3]
  Answer: ¬(¬A) = A by double negation (1); B ∧ ¬B = 0 by the complement law (1); A ∨ 0 = A by the identity law, so the answer is A (1).
3. Use De Morgan's law to rewrite ¬(A ∨ ¬B) without a bracket. [2]
  Answer: Break the bar, swap ∨ for ∧ and negate each term: ¬A ∧ ¬(¬B) (1); double negation gives ¬A ∧ B (1).
4. State the input combinations for which Q = ¬A ∧ (B ∨ C) is 1. [2]
  Answer: Q = 1 requires A = 0 and at least one of B, C to be 1 (1): the rows A=0 B=0 C=1, A=0 B=1 C=0 and A=0 B=1 C=1 (1). All other five rows give 0.

## Slide 24
Practice (5-8)
1. Simplify A ∨ (A ∧ B) and name the law used. [2]
2. State the commutative law and the associative law for the ∧ operator. [2]
3. Show that A ∧ (B ∨ ¬A) simplifies to A ∧ B, naming each law. [3]
4. A student claims ¬(A ∧ B) = ¬A ∧ ¬B. Use the row A = 1, B = 0 to show the claim is false, and state the correct law. [3]

## Slide 25
Practice — answers (5-8)
1. Simplify A ∨ (A ∧ B) and name the law used. [2]
  Answer: A (1), by the absorption law (1).
2. State the commutative law and the associative law for the ∧ operator. [2]
  Answer: Commutative: A ∧ B = B ∧ A, the order of operands does not matter (1). Associative: (A ∧ B) ∧ C = A ∧ (B ∧ C), the grouping does not matter (1).
3. Show that A ∧ (B ∨ ¬A) simplifies to A ∧ B, naming each law. [3]
  Answer: Distribution: A ∧ (B ∨ ¬A) = (A ∧ B) ∨ (A ∧ ¬A) (1); complement law: A ∧ ¬A = 0 (1); identity law: (A ∧ B) ∨ 0 = A ∧ B (1).
4. A student claims ¬(A ∧ B) = ¬A ∧ ¬B. Use the row A = 1, B = 0 to show the claim is false, and state the correct law. [3]
  Answer: At A=1, B=0: ¬(A ∧ B) = ¬0 = 1 (1) but ¬A ∧ ¬B = 0 ∧ 1 = 0, so the two differ (1). The correct law is ¬(A ∧ B) = ¬A ∨ ¬B: the operator must swap when the bar breaks (1).

## Slide 26
Common misconceptions
✗ Students often think De Morgan's law just swaps the operator; you must also negate each variable, otherwise the row A=1, B=0 breaks the claim.
✗ Students often treat OR and XOR as the same; they differ in exactly one row: both inputs 1 gives OR = 1 but XOR = 0.
✗ Students often think only AND distributes over OR, as in ordinary algebra; in Boolean algebra OR also distributes over AND: A ∨ (B ∧ C) = (A ∨ B) ∧ (A ∨ C).
✗ Students often write ¬A ∧ B when they mean ¬(A ∧ B); without a bracket, ¬ binds only to the variable next to it.
✗ Students often build truth tables with missing or misordered rows; n inputs need exactly 2 to the power n rows, counted in binary from all zeros.

## Slide 27
How the exam asks this
Command words seen here: complete for truth tables (2-4 marks), simplify for expressions (2-4 marks, with laws named), show that for proving equivalences (3 marks).
OCR uses ∧, ∨, ¬ and ⊻ on the paper; you may write A·B and A+B, but you must read the exam's notation fluently.
Simplification mark schemes award the working: name the law at each step, because a correct answer with no laws can lose marks.
Example stem: 'Complete the truth table for the circuit Q = (A ∨ B) ∧ ¬C, then simplify ¬(¬A ∧ ¬B) using De Morgan's law.' [6]

## Slide 28
Your turn
Task
  Complete the full 8-row truth table for Q = ¬(A ∧ B) ∨ (A ∧ C), showing working columns for A ∧ B, ¬(A ∧ B) and A ∧ C, and identify the only row where Q = 0. (Answer: Q column down rows 000 to 111 is 1, 1, 1, 1, 1, 1, 0, 1; the only 0 is at A=1, B=1, C=0, because there ¬(A ∧ B) = 0 and A ∧ C = 0.)
Challenge / stretch
  Simplify ¬(¬A ∨ ¬B) ∨ (A ∧ ¬B) as far as possible, naming the law at every step, and verify your answer with two truth-table rows. (De Morgan's plus double negation: ¬(¬A ∨ ¬B) = A ∧ B; distribution: (A ∧ B) ∨ (A ∧ ¬B) = A ∧ (B ∨ ¬B); complement: B ∨ ¬B = 1; identity: A ∧ 1 = A. Check A=1 B=0: original = 0 ∨ 1 = 1 = A; check A=0 B=1: original = 0 ∨ 0 = 0 = A.)

## Slide 29
Exit ticket
1. Rewrite ¬(A ∧ B) using De Morgan's law.
2. What does A ⊻ B output when A = 1 and B = 1, and why?
3. Simplify A ∧ (A ∨ B) and name the law used.

## Slide 30
Exit ticket — answers
1. Rewrite ¬(A ∧ B) using De Morgan's law.
  Answer: ¬A ∨ ¬B: break the bar, change ∧ to ∨, negate each variable.
2. What does A ⊻ B output when A = 1 and B = 1, and why?
  Answer: 0, because XOR outputs 1 only when its inputs differ.
3. Simplify A ∧ (A ∨ B) and name the law used.
  Answer: A, by the absorption law.