## Slide 1
1.4.3 Boolean Algebra
OCR H446 — Component 01
Lesson deck — editable skeleton: adapt freely.

## Slide 2
Learning objectives
By the end of this lesson you can:
  Construct truth tables for logic gates and combined expressions, including AND, OR, XOR, NAND and NOR.
  Simplify Boolean expressions using identities, De Morgan's laws and Karnaugh maps.
  Describe the operation of half adders, full adders and D-type flip-flops, distinguishing combinational and sequential logic.

## Slide 3
Do Now — retrieval starter
1. Which two gates are described as universal?
2. State De Morgan's law for NOT(A + B).
3. What does a D-type flip-flop do?
4. Interleaving (1.4.1): What is the place value of the MSB in an 8-bit two's complement number?
5. Interleaving (1.4.2): Which BST traversal outputs nodes in ascending order?

## Slide 4
Do Now — answers
1. Which two gates are described as universal?
  Answer: NAND and NOR.
2. State De Morgan's law for NOT(A + B).
  Answer: NOT(A + B) = NOT A AND NOT B (break the bar and swap OR for AND).
3. What does a D-type flip-flop do?
  Answer: It stores one bit of data on an active clock edge and presents it at Q until the next edge.
4. Interleaving (1.4.1): What is the place value of the MSB in an 8-bit two's complement number?
  Answer: -128.
5. Interleaving (1.4.2): Which BST traversal outputs nodes in ascending order?
  Answer: In-order (left, root, right).

## Slide 5
Key terminology
Truth table — A table listing the output of a logic expression for every possible combination of input values.
XOR — Exclusive-OR gate that outputs 1 only when its inputs differ, written A XOR B.
Universal gate — A gate from which any logic circuit can be built; NAND and NOR are universal.
De Morgan's laws — NOT(A.B) = NOT A + NOT B and NOT(A+B) = NOT A . NOT B; break the bar and swap AND with OR, negating each variable.
Absorption law — A + A.B = A and A.(A+B) = A; a redundant term is absorbed.
Half adder — A circuit adding two bits with no carry-in: Sum = A XOR B, Carry = A . B.
Full adder — A circuit adding three bits (A, B, Cin): Sum = A XOR B XOR Cin, Cout = (A.B) + (Cin.(A XOR B)); chained to form a ripple-carry adder.
D-type flip-flop — An edge-triggered 1-bit memory (sequential logic) that stores input D on a clock edge and synchronises data to the clock.

## Slide 6
Logic gates and truth tables
AND outputs 1 only when both inputs are 1; OR outputs 1 when at least one input is 1.
XOR outputs 1 when inputs differ; NAND is NOT(A.B) and NOR is NOT(A+B), the negations of AND and OR.
NAND and NOR are universal, meaning any circuit can be built from copies of either gate alone.

## Slide 7
Boolean identities
Identity and null: A.1 = A, A+0 = A, A.0 = 0, A+1 = 1.
Idempotent A.A = A, complement A.NOT A = 0 and A + NOT A = 1, double negation NOT(NOT A) = A.
Distributive A.(B+C) = A.B + A.C, and absorption A + A.B = A help reduce expressions.

## Slide 8
De Morgan's laws and K-maps
De Morgan's: break the bar, change the operator (AND to OR or OR to AND) and negate each variable, then tidy with double negation.
K-maps plot outputs in a grid where adjacent cells differ by one variable.
Group adjacent 1s in powers of two (1, 2, 4, 8...), as large as possible, allowing wrap-around and overlap, to read off a minimal sum-of-products.

## Slide 9
Adders
A half adder adds two bits with no carry-in: Sum = A XOR B, Carry = A . B.
A full adder adds three bits: Sum = A XOR B XOR Cin, Cout = (A.B) + (Cin.(A XOR B)).
Full adders are chained so each carry-out feeds the next column's carry-in, forming a ripple-carry adder for multi-bit numbers.

## Slide 10
Combinational vs sequential logic
Combinational logic outputs depend only on the current inputs, e.g. gates and adders.
Sequential logic outputs depend on inputs plus stored state, e.g. circuits using flip-flops.
A D-type flip-flop is edge-triggered 1-bit memory used in registers, counters and memory cells to synchronise data to a clock.

## Slide 11
Worked example
Simplifying NOT(NOT A + B) with De Morgan's law
  1. Start with the expression NOT(NOT A + B), which has an outer bar over an OR.
  2. Apply De Morgan's to the outer bar: break the bar and change OR to AND, negating each term, giving NOT(NOT A) . NOT B.
  3. Apply double negation to the first term: NOT(NOT A) = A.
  4. The expression becomes A . NOT B.
  5. Check with a truth table: NOT(NOT A + B) is 1 only when A=1 and B=0, which is exactly when A . NOT B = 1, confirming the result.
  6. Final simplified form: A . NOT B.

## Slide 12
Your turn
Task
  Complete the truth table for Q = NOT(A.B) + (A.C) over all eight input combinations of A, B and C, and identify the only row where Q = 0.
Challenge / stretch
  Give the Boolean expressions for the Sum and Cout of a full adder, then explain how it differs from a half adder and why full adders (not half adders) are needed to add multi-bit binary numbers.

## Slide 13
Exit ticket
1. Rewrite NOT(A.B) using De Morgan's law.
2. What are the Sum and Carry outputs of a half adder when A=1 and B=1?
3. Simplify A.(A+B) and name the law used.

## Slide 14
Exit ticket — answers
1. Rewrite NOT(A.B) using De Morgan's law.
  Answer: NOT A + NOT B.
2. What are the Sum and Carry outputs of a half adder when A=1 and B=1?
  Answer: Sum = 0 and Carry = 1 (binary 10), since Sum = A XOR B and Carry = A . B.
3. Simplify A.(A+B) and name the law used.
  Answer: It simplifies to A by the Absorption law.